## Slide 1
Dr. Mehak Ahuja
Assistant Professor, Department of Chemistry
School of Basic and Applied Sciences
K.R. Mangalam University
Sohna Road, Gurugram
Introduction to Water Chemistry & Hardness
Course Code: ETMLCH104
Course Name: Engineering Chemistry
Program: B.Tech. (AI/ML)
Unit 3: Battery Technology

## Slide 2: Course Overview
UNIT WISE DETAILS ​ ​ ​ |  | 
Unit Number: 1 ​ | Title: Water technology ​ | No. of hours: 6 ​
Content Summary: ​ Introduction, water analysis: Hardness-determination by EDTA method, Treatment of boiler feed water: Internal treatment (Phosphate, Colloidal and Calgon conditioning). External treatments: Ion exchange and lime-soda process, Zeolite processes. Boiler scales formation and ill effects, methods of prevention of scales. Numerical problems ​ |  | 
Unit Number: 2 ​ | Title: Chemical Fuels ​ | No. of hours: 9 ​
Content Summary: ​ Fuels: Introduction, classification, calorific value (HCV & LCV), Determination of calorific value of fuel using Bomb calorimeter. ​ Solid fuel: Coal- its analysis by proximate and ultimate analysis, Numerical problems. ​ Liquid fuels: Refining of petroleum, Petroleum cracking, Knocking in IC engine, its ill effects and prevention of knocking. Anti-knocking agent: Leaded and unleaded petrol. ​ Gaseous fuels: LPG, CNG and their applications. ​ |  | 
Unit Number: 3 ​ | Title: Battery Technology ​ | No. of hours: 10 ​
Content Summary: ​ Introduction - Galvanic cell, electrode potential, EMF of the cell and cell representation. Batteries and their importance, Classification of batteries- primary, secondary and reserve batteries with examples. Battery characteristics - voltage, capacity, energy density, power density, energy efficiency, cycle life and shelf life. ​ Construction, working and applications of: Ni-Cd, and Lithium-ion battery. Working principle of an electric vehicle. ​ |  | 
Unit Number: 4 ​ | Title: Polymer ​ | No. of hours: 5 ​
Content Summary: ​ Basic concepts of polymer, Types of polymers, Thermoplastic & thermosetting plastics, Preparation and application of some industrially important polymers (Natural rubber, Buna S, Buna-N, Neoprene, Isoprene, Nylon-6, nylon-6,6 , Decron and Terylene). Conducting and biodegradable polymers. ​ |  | 

## Slide 3
COURSE OUTCOMES
CO1: Understand the methods for water hardness and the basics of boiler water treatment and analyze fuel calorific values and battery.
CO2: Explain the characteristics and working principles of different battery types and types of fuels.
CO3: Determine the differences between batteries and fuel cells and classify fuel cell types based on their components..
CO4: Identify between hard and soft water, solve the related numerical problems on water purification and emf and its significance in industry and daily life.

## Slide 4: Battery Technology
Introduction - Galvanic cell, electrode potential, EMF of the cell and cell representation.

## Slide 5
Electrochemical cells
Electrochemical cells are devices that convert chemical energy into electrical energy or vice versa.
Galvanic cells (also called voltaic cells) are electrochemical cells that produce electrical energy from a spontaneous redox reaction.
Electrode potential is the tendency of an electrode to lose or gain electrons.
EMF (electromotive force) is the maximum potential difference between two electrodes of a galvanic cell when no current is flowing.
Cell representation is a shorthand way of representing a galvanic cell, showing the electrodes, electrolyte, and direction of electron flow.
Notes: New Courses replaced with New Programmes

## Slide 6
Difference between Galvanic cell and Electrolytic cell
Fig 1 : Galvanic cell and electrolytic cell

## Slide 15
Galvanic cell diagram
Fig 2 : Galvanic cell representation
Notes: New Courses replaced with New Programmes

## Slide 16
Example:
Write the half-cell reaction and the overall cell reaction for the electrochemical cell: Zn | Zn 2+ (1.0M) || Pb 2+ (1.0M) | Pb
Calculate the standard e.m.f for the cell if standard electrode potential (reduction) for Pb 2+ | Pb and Zn 2+ | Zn electrodes are – 0.126 V and – 0.763 V respectively.
Zn electrode acts as anode
Pb electrode acts as cathode
And therefore , oxidation occurs at zinc electrode and reduction occurs at lead electrode.
The half cell reactions are : Oxidation half reaction : Zn(s)→Zn2+(aq)+2e− Reduction half reaction : Pb2+(aq)+2e− →Pb(s)
Overall cell reaction : Zn (s) +Pb2+(aq)→Zn2+(aq) + Pb(s) Eocell= EoR−EoL = −0.126−(−0.763) =0.637 V
Notes: New Courses replaced with New Programmes

## Slide 19: Take away of the session
Definition: A battery is a device that stores chemical energy and converts it into electrical energy through electrochemical reactions.
Types of Batteries:
Primary Batteries: Non-rechargeable (e.g., dry cell, alkaline battery)
Secondary Batteries: Rechargeable (e.g., lead-acid, lithium-ion, nickel-cadmium)
Key Components:
Anode (negative electrode)
Cathode (positive electrode)
Electrolyte (medium for ion flow)
Important Parameters:
Voltage, capacity (mAh/Ah), cycle life, energy density, charging time
Applications: Widely used in electronics, EVs, power backup systems, and renewable energy storage.

## Slide 20
1. Which of the following batteries is rechargeable? A. Alkaline battery B. Dry cell C. Lead-acid battery D. Zinc-carbon battery ✅ Answer: C
2. What is the function of the electrolyte in a battery? A. Stores electricity B. Prevents short circuit C. Allows ion flow between electrodes D. Insulates the electrodes ✅ Answer: C
3. Which of the following is a primary battery? A. Nickel-cadmium battery B. Lead-acid battery C. Lithium-ion battery D. Zinc-carbon battery ✅ Answer: D
4. What does “mAh” (milliampere-hour) indicate in a battery? A. Voltage rating B. Power consumption C. Battery capacity D. Resistance ✅ Answer: C
5. Lithium-ion batteries are widely used in: A. Flashlights B. Mobile phones and laptops C. Remote controls D. Emergency lamps only ✅ Answer: B
Questions

## Slide 21: Learning Outcomes
CO1: Understand the methods for water hardness and the basics of boiler water treatment and analyze fuel calorific values and battery.
CO2: Explain the characteristics and working principles of different battery types and types of fuels.
Mapped Course Outcomes
BTL-1: Recall definitions and types of electrochemical cells and batteries (CO1, CO2)
BTL-2: Explain the construction and characteristics of batteries and galvanic cells (CO1, CO2)
BTL-3: Apply EMF calculation methods and relate them to real battery examples (CO1)
BTL-4: Analyze the differences between galvanic and electrolytic cells (CO2)

## Slide 22: References
Engineering Chemistry by Jain and Jain.