## Slide 1
Dr Pratibha Sharma
Assistant Professor, Department of Chemistry
School of Basic and Applied Sciences
K.R. Mangalam University
Sohna Road, Gurugram
Introduction to Water Chemistry & Hardness
Course Code: ETMLCH104
Course Name: Engineering Chemistry
Program: B.Tech. (AI/ML)
Unit1:Water technology & Chemical Fuels

## Slide 2: Course Overview
Unit Number: 1 | Title: Water technology | No. of hours: 6
Introduction, water analysis: Hardness-determination by EDTA method, Treatment of boiler feed water: Internal treatment (Phosphate, Colloidal and Calgon conditioning). External treatments: Ion exchange and lime-soda process, Zeolite processes. Boiler scales formation and ill effects, methods of prevention of scales. Numerical problems |  | 
Unit Number: 2 | Title: Chemical Fuels | No. of hours: 9
Fuels: Introduction, classification, calorific value (HCV & LCV), Determination of calorific value of fuel using Bomb calorimeter. Solid fuel: Coal- its analysis by proximate and ultimate analysis, Numerical problems. Liquid fuels: Refining of petroleum, Petroleum cracking, Knocking in IC engine, its ill effects and prevention of knocking. Anti-knocking agent: Leaded and unleaded petrol. Gaseous fuels: LPG, CNG and their applications. |  | 
Unit Number: 3 | Title: Battery Technology | No. of hours: 10
Introduction - Galvanic cell, electrode potential, EMF of the cell and cell representation. Batteries and their importance, Classification of batteries- primary, secondary and reserve batteries with examples. Battery characteristics - voltage, capacity, energy density, power density, energy efficiency, cycle life and shelf life. Construction, working and applications of: Ni-Cd, and Lithium-ion battery. Working principle of an electric vehicle. |  | 
Unit Number: 4 | Title: Polymer | No. of hours: 5
Basic concepts of polymer, Types of polymers, Thermoplastic & thermosetting plastics, Preparation and application of some industrially important polymers (Natural rubber, Buna S, Buna-N, Neoprene, Isoprene, Nylon-6, nylon-6,6 , Decron and Terylene). Conducting and biodegradable polymers. |  | 

## Slide 3
COURSE OUTCOMES
CO1: Understand the methods for water hardness and the basics of boiler water treatment and analyze fuel calorific values and battery.
CO2: Explain the characteristics and working principles of different battery types and types of fuels.
CO3: Determine the differences between batteries and fuel cells and classify fuel cell types based on their components..
CO4: Identify between hard and soft water, solve the related numerical problems on water purification and emf and its significance in industry and daily life.

## Slide 4: External Treatment Method
Lime-soda Process

## Slide 5
Techniques for water softening (External treatment)
Lime-soda process
  Hot-Lime Soda process
  Cold-Lime Soda process
Zeolite Process
Ion-Exchange Method
  Cation-exchange
  Anion-exchange

## Slide 8
Techniques for water softening (External treatment)
Lime-soda process:
In this process, hydrated lime & sada ash use to remove hardness from water.
i) Hydrated lime:
Hydrated lime is used to remove temporary hardness of water. It react with Ca(HCO3)2 & Mg(CO3)2 to form insoluble precipitate of calcium carbonate and magnesium hydroxide respectively.
Ca(HCO3)2 + Ca(OH)2 2CaCO3↓ + 2H2O
Mg(HCO3)2 + 2Ca(OH)2 Mg(OH)2↓ + 2CaCO3↓ + 2H2O
Hydrated lime is also used to remove permanent hardness (magnesium salt impurities only) from water. It reacts with MgSO4 & MgCl2 to form insoluble precipitate of magnesium hydroxide.
MgCl2 + Ca(OH)2 Mg(OH)2↓ + CaCl2
MgSO4 + Ca(OH)2 Mg(OH)2↓ + CaSO4

## Slide 9
Techniques for water softening (External treatment)
In above reaction calcium based impurities like CaCl2 & CaSO4 also form, which are soluble in water. Therefore, calcium based impurities (CaCl2 & CaSO4) are not removed by lime treatment.
ii) Soda ash:
Sodium carbonate (Na2CO3) is used to remove permanent hardness of water which caused by MgSO4 & MgCl2 or CaCl2 & CaSO4.
CaCl2 + Na2CO3 CaCO3↓ + 2NaCl
CaSO4 + Na2CO3 CaCO3↓ + Na2SO4
MgCl2 + Na2CO3 MgCO3↓ + 2NaCl
MgSO4 + Na2CO3 MgCO3↓ + Na2SO4

## Slide 10
Techniques for water softening (External treatment)
The amount of lime-soda required for the softening of hard water can be calculated by following formula-

## Slide 12
Techniques for water softening (External treatment)

## Slide 13: Hot Lime Soda Process

## Slide 14
Techniques for water softening (External treatment)

## Slide 16: Take away of the session
Purpose: Removes hardness from water using chemical precipitation.
Chemicals Used: Lime (Ca(OH)₂) removes temporary hardness; soda ash (Na₂CO₃) removes permanent hardness.
Process: Hardness-causing ions form insoluble precipitates (e.g., CaCO₃, Mg(OH)₂) which are then removed.
Types: Cold lime-soda (room temp) and hot lime-soda (better efficiency due to higher temp).
Applications: Commonly used for municipal and industrial water softening.

## Slide 17: Questions
What is the main purpose of the lime-soda process? A. Disinfection of water B. Removal of turbidity C. Softening of hard water D. pH adjustment
Which chemical is used in the lime-soda process to remove temporary hardness? A. Na₂CO₃ B. Ca(OH)₂ C. HCl D. K₂SO₄
What is the role of soda ash (Na₂CO₃) in the process? A. Removes magnesium hardness B. Acts as a coagulant C. Removes permanent calcium hardness D. Increases water pH
Which of the following is an advantage of the hot lime-soda process over the cold one? A. Lower efficiency B. Slower reaction rate C. Better removal of hardness D. Lower cost of operation
What is formed as a precipitate when lime reacts with temporary hardness? A. NaCl B. CaSO₄ C. MgCl₂ D. CaCO₃

## Slide 18: References
Engineering Chemistry by Jain and Jain.